## Slide 1: Linking BIM and GIS Standard Ontologies with Linked Data
Elio Hbeich & Ana Roxin
17-19 June 2020, Dublin, Ireland

## Slide 2: Summary
Introduction
BIM Standard Ontology
GIS Standard Ontologies
Related Work
Our Approach
Conclusion
Usefulness and Future Work

## Slide 3: Introduction
Building Information Model (BIM)
Geographic Information System (GIS)
Need : seamless data interpretation
BIM standard Ontology
GIS standard Ontologies
No semantic links defined
EXPRESS to OWL translation
UML to OWL translation
IfcOWL (IFC4_ADD1)
ISO/TC 211 Ontologies
Notes: While Building information model is conceived to handles building information with high level of detailed from design to demolition,
GIS handles data concerning natural environment with a lower level of details.
Even though both domains are used for distinctive situations and objectives they are complementary.
In order to combine their advantages, create seamless reasoning in application context, and place building in urban context we need to achieve seamless data interoperation.
To do so, we transform data into knowledge through semantic web approaches (ontologies) and create semantic link among concepts and properties.
In the context of this presentation , we are solely aiming at linking standard ontologies in BIM and GIS domains, which are the ifcOWL ontology for IFC
and the ontologies defined by ISO/TC 211 for the ISO 19100 standard family.

## Slide 4: The Issue
3 layers of data interoperability
  Physical (e.g. network protocols )
  Syntactic (e.g. XML)
  Semantic (e.g. RDF, OWL)
Ontologies represent the building blocks of semantic interoperability still only adopting ontologies does not fully solve semantic heterogeneity issue (Farias et al., 2015)
BIM and GIS existing standard ontologies must be semantically aligned for allowing seamless interpretation of BIM/GIS models e.g. urban use case scenarios
Farias T.M., Roxin A., Nicolle C. (2015) FOWLA, A Federated Architecture for Ontologies. In: Bassiliades N., Gottlob G., Sadri F., Paschke A., Roman D. (eds) Rule Technologies: Foundations, Tools, and Applications. RuleML 2015. Lecture Notes in Computer Science, vol 9202. Springer, Cham
Notes: Because different ontology might represent the same or similar knowledge in different tasks or requirements and follow different conventions and restrictions.
These differences can be categories in what we call ontologies heterogeneity, and divided into the following (Pak & Zhou, 2010):
Syntactical heterogeneity: available in different ontology representation languages and can be resolved on the conceptual level (OWL 2DL vs. OWL 2 EL)
Terminological heterogeneity: concerns naming differences for the identification of entities in different ontologies and might occur because different languages are used (French, English, etc.)
Conceptional / semantic heterogeneity: concerns ontologies that modeled the same domain, but in different ways, it manifests in different coverage, granularity, perspective, etc.
Semiotic / pragmatic heterogeneity: concerns differences interpretation of the domain modeled by humans.
Because BIM and GIS ontologies are represented on OWL languages Syntactical heterogeneity is solved that is why our work tackles terminological heterogeneity.

## Slide 5: BIM Standard Ontology – ifcOWL
ifcOWL has the following characteristics:
  OWL2DL
  Matches the original EXPRESS schema,
  Allows the conversion of IFC STEP files into equivalent RDF graphs.
EXPRESS
OWL
Algorithm in Java and C++
Simple data types
Defined data types
List aggregation data types,
Array aggregation data types
Etc.
Class hierarchy,
Object properties
Etc.
IFC
ifcOWL
Notes: BIM is a combination of process, methods and 3D parametric digital model. It aims at supporting, sharing reliable information throughout the life cycle of the considered element. It relies on the following standards:
IDM: specify communication and data exchange requirements during a projects life cycle.
MVD: predefine the amount of the model required to support a specific stage of the project, and describe the data model needed to meet the exchange requirements
IFC: comes with data schema and exchange file structures that provide the guidelines to determine what information is exchange about an asset. In addition the IFC data is structure according to express specification.
As previously said the BIM ontology will be generated from IFC. The main BIM ontology is the one generated by Pieter and Walter.
Where they implement a conversion pattern (algorithm) provided in Java and C++ to convert the considered EXPRESS schema (simple, defined, list aggregation, array aggregation data types, etc.) into OWL (OWL class hierarchy, object properties, etc.). The generated ifcOWL ontology is in OWL2 DL, matches the original EXPRESS schema, and allows the conversion of IFC STEP files into equivalent RDF graphs.

## Slide 6: GIS Standard Ontologies
ISO
19104
ISO
19130
ISO
19131
Conceptual Application Schemas
ISO
19101
ISO
19109
ISO
19103
Metamodel
ISO
19116
ISO
19117
ISO
19118
ISO
19119
ISO
19126
ISO
19128
ISO
19129
ISO
19132
ISO
19133
ISO
19134
ISO
19150
ISO
19159
ISO
19160
Implementation Schemas
ISO
19107
ISO
19108
ISO
19110
ISO
19111
ISO
19112
ISO
19115
ISO
19123
ISO
19137
ISO
19141
Conceptual Abstract Schemas
ISO
19148
ISO
19157
ISO 19109:2015 Geographic information — Rules for application schema
ISO 19111:2007 Geographic information — Spatial referencing by coordinates
ISO/TS 19130:2010 Geographic information - Imagery sensor models for geo-positioning
Notes: GIS allows to create, manipulate, store and display information based on its location.
GIS conceptual architecture is defined by model-driven architecture where each ISO standard is contained in a different level of abstraction.
Metamodel: specifies the concepts, terminology operation and assumptions needed to specify the basic construct. It contains the following standards (name some of the above standards)
Conceptual abstract schema: defines all detail needed to tailor a software system to a specific application. It contains the following standards (name some of the above standards).
Conceptual application schema: defines types of features and process that a instantiated to reduce datasets of geographic information. It contains the following standards (name some of the above standards)
Implementation schema: includes the actual data. It contains the following standards (name some of the above standards)
ISO/TC 211 Ontologies are maintained and published by GOM, they are generated from UML based on the rules and guidelines defined In ISO 19150.

## Slide 7: Related Work
No previous approach created links between BIM and ISO/TC 211standards ontologies
Reference | Description | Limits
Kang. S et al., 2019 [1] | Introduces BIM to GIS (B2G) mapping by applying perspective definition (B2G PD), element mapping (B2G EM) and LoD mapping (B2G LM) mechanisms. | Maps only building models Promotes one domain over the other by implementing integration approach
Donkers. S, 2013 [2] | Works on automatically generating CityGML building models from IFC using Semantic Web Technology by mapping different entities and properties. | Generates data loss Promotes one domain into the other Generates only CityGML LoD 3 building model
El-Mekawy et al., 2019 [3] | Semantically integrates IFC and CityGML by conceiving the UBM ontology (Unified Building Model). Trandofmration rules were used for creating semantic relationships between IFC and CityGML. | Most mappings focus on IfcProductExtension and the IFC concepts in the interoperability layer Focuses on building model Promotes one domain over the other
[1] Kang, T. Development of a Conceptual Mapping Standard to Link Building and Geospatial Information. ISPRS International Journal of Geo-Information. (2018).
[2] Donkers, S. Automatic generation of CityGML LoD3 building models from IFC models. (2013)
[3] El-Mekawy, M., & Östman, A. Semantic Mapping: an Ontology Engineering Method for Integrating Building Models in IFC and CityGML. In the 3rd ISDE Digital EART Summit, Nessebar, Bulgaria (2010).
Notes: NO previous study has created or suggested any link between BIM and ISO/TC 211 Ontologies.
In this slide we are going to present related studies that connected BIM to GIS application based on semantic link technologies.
(talk about [1], [2], [3]) and their limits.
Generate data loss
Present solution for a specific use case
Map only building models
Promote one domain over the other.
Most mapping concentrate only on IfcProductExtension and the IFC concepts in the interoperability layer
[1], [2] implement integration approach, while [3] implement unification approach
No previous work have used the federation approach

## Slide 8: Related Work
Notes: Several researches have tackled improving the standard ifcOWL ontology. [1] proposed IfcWoD that comes with two main advantages compared to the standard ifcOWL version: (1) EXPRESS collections are mapped as OWL properties instead of RDF or OWL Lists, and (2) IFC defined types aren't directly converted into classes. [3] transforms the Construction Operations Building Information Exchange (COBie) standard into the COBieOWL ontology and aligned it to ifcOWL ontology by transforming the COBie MVD into SWRL rules. Furthermore, IFC ontology is linked to other building ontologies, for example [3] presents mapping results between BOT (Building Topology Ontology) and other building ontologies such as IFC, SAREF4BLDG (SAREF Ontology for Building), and BRICK.
Our contribution aim to establish semantic links between BIM and ISO/TC 211 domains through Semantic Web Technologies

## Slide 9: Our Approach
As mentioned in our previous publication (Roxin. A, & Hbeich. E. 2019) and in order to connect BIM and GIS knowledge representations we are aiming to define semantic links among:
Roxin. A, & Hbeich. E. Semantic interoperability between BIM and GIS – review of existing standards and depiction of a novel approach. 36th CIB W78 – Information Technology for Construction, Newcastle, United Kingdom. (2019).
ISO 19111
ISO 19130
ISO 19109
Notes:   As mentioned in our previous publication (Roxin. A, & Hbeich. E. 2019)
  and in order to connect BIM and GIS knowledge representations we are aiming to define semantic links among:
  Link GIS Metamodel (e.g. ISO 19109) and IFC Core Layer.
  Link GIS abstract conceptual schemas (e.g. ISO 19111, ISO 19107) and IFC Resource Definition Layer.
  Link GIS application schemas (e.g. ISO 19130, ISO 19131) and IFC Domain Specific and Shared Elements
  Due to time limit I going to choice one standard of each layer and present the semantic mapping links proposed with the appropriate IFC layer

## Slide 10: Linking GIS Metamodel and IFC Core Layer
IFC4_ADD1.owl | Relation | ISO 19109.owl
IFC4.1:IfcRoot | owl:equivalentClass | ISO19109:AnyFeature
IFC4.1:IfcProductExtension | owl:equivalentClass | ISO19109:AttributeType
IFC Core Layer | Description | ISO 19109 | Description
IfcRoot | IfcRoot is the most abstract and root class for all entity definitions that roots in the kernel or in subsequent layers of the IFC specification. It is therefore the common super type of all IFC entities, beside those defined in an IFC resource schema | Any Feature | It represents the set of all classes which are feature types
IfcProduct Extension | Further specializes the concepts of a (physical) product, i.e. a component likely to have a shape and a placement within the project context | Attribute Type | It recognizes all kinds of attributes: temporal, spatial geometry, spatial topology, data quality, generic metadata, and location.
Prefix :
ISO19109 ="http://def.isotc211.org/iso19109/2015/ RulesForApplicationSchema #”
IFC4.1 = "http://ifcowl.openbimstandards.org/IFC4_ADD1#"

## Slide 11: Linking GIS Abstract Schemas and IFC Resource Definition Layer
IFC4_ADD1.owl | Relation | ISO 19111.owl
IFC4.1:IfcProjectedCRS | owl:equivalentClass | ISO19111:ProjectedCRS
IFC4.1:IfcCoordinate ReferenceSystem | owl:equivalentClass | ISO19111:CoordinateSystem
IFC4.1:refDirection_ IfcAxis2Placement3D | owl:equivalentProperty | ISO19111:CoordinateSystemAxis. axisDirection
IFC Resource Layer | Description | ISO 19111 | Description
IfcCoordinateReference System | It is a definition of a coordinate reference system using qualified identifiers only. | CoordinateSystem (CS) | It is the non-repeating sequence of coordinate system axes that span a given coordinate space. A CS is derived from a set of mathematical rules for specifying how coordinates in each space are to be assigned to points.
IfcProjectedCRS | It is a coordinate reference system of the map to which the map translation of the local engineering coordinate system of the construction or facility engineering project relates. | ProjectedCRS | It is a derived coordinate reference system which has a geodetic coordinate reference system as its base CRS and is converted using a map projection.
IfcAxis2Placement 3D | Provides location and orientations to place items in a three-dimensional space. The attribute Axis defines the Z direction, RefDirection the X direction, the Y direction is derived. | Coordinate SystemAxis | Defines coordinate system axis (axisAbbre, axeDirection, axe UnitID).
Prefix :
ISO 19111= "http://def.isotc211.org/iso19111/2019/CoordinateReferenceSystems#"
IFC4.1 = "http://ifcowl.openbimstandards.org/IFC4_ADD1#"

## Slide 12: Linking GIS Application Schemas and IFC Domain Specific and Shared Elements Layers
IFC4_ADD1.owl | Relation | ISO 19130.owl
IFC4.1: IfcTimeMeasure | owl:equivalentProperty | ISO19130: SD_Dynamics. dateTime
IFC4.1: IfcDimensionCount | owl:equivalentProperty | ISO19130:SD_DetectorArray. numberOfDimensions
IFC Shared Element Layer Schemas | Description | ISO 19130 | Description
IfcTimeMeasure | It is the value of the duration of periods. Measured in seconds (s) or days (d) or other units of time. | dateTime | It is the time value of the taken measurement
IfcDimensionCount | It defines the dimensionality of the coordinate space. It is restricted to have the dimensionality of either 1, 2, or 3 for the purpose of this specification | numberofDimensions | Number of dimension
Prefix :
ISO 19130= "http://def.isotc211.org/iso19130/2018/SensorData#"
IFC4.1 = "http://ifcowl.openbimstandards.org/IFC4_ADD1#"

## Slide 13: Conclusion
We aim to achieve seamless data interpretation by creating semantic links between BIM and GIS standards knowledge representation (IFC for BIM and ISO/TC 211 for GIS).
As both knowledge domains are represented using OWL language, we focused on creating semantic links based on concepts and properties definitions, thus tackling terminological heterogeneity.
Our work will be useful only through the acknowledgment of the scientific communities such as LDAC and the actual implementation of the semantic links from both domains (BIM ISO/TC59/SC13 and GIS ISO/TC211)

## Slide 14: Usefulness and Future Work
Usefulness:
  The mapping is not limited to a specific use case.
  Both domains remain independent from each other.
  Reduce heterogeneity between both domains ontologies.
Future Work:
  Confront conceptual and semiotic heterogeneities mapping between BIM and GIS ontologies.
  Define mediator ontologies which establish terminological equivalences among schemas.
  Define of complex semantic mappings: which require exchanges with business experts.
  Integrate previous mappings created by the community.
Notes: Usability:
In case those mapping are adopted (by the scientific community) it could enable us to map both knowledge with out the limitation of use case, keep both domains independent because no Metamodel is created or used as a reference model
Future work:
(read the points)

## Slide 15
Thank you for your attention
QUESTIONS?
Contacts:
elio.hbeich@cstb.fr
ana-maria.roxin@ubfc.fr