## Slide 1
Linked Data for Smart Homes
Comparing RDF and LPG
Alex Donkers MSc – PhD Candidate at Eindhoven University of Technology – a.j.a.donkers@tue.nl

## Slide 2
Smart homes
Health monitoring
IoT data integration
Activity recognition
Social media integration
Energy efficiency
Indoor environmental quality
Home automation
Building performance monitoring
Different domain knowledge
Many stakeholders
Siloed data

## Slide 3
We need to compare
RDF with other graph models

## Slide 4: Graph models
Undirected graph
Simple graph
Multi-graph
Halve-edge graph
Labeled graph
Weighted graph
Property graph
Labeled property graph
Hypergraph
RDF
RDF*
Kitchen
Toilet
- labels

## Slide 5: Graph models
Undirected graph
Simple graph
Multi-graph
Halve-edge graph
Labeled graph
Weighted graph
Property graph
Labeled property graph
Hypergraph
RDF
RDF*
no labels
directed edges

## Slide 6: Graph models
Undirected graph
Simple graph
Multi-graph
Halve-edge graph
Labeled graph
Weighted graph
Property graph
Labeled property graph
Hypergraph
RDF
RDF*
multiple directed edges

## Slide 7: Graph models
Undirected graph
Simple graph
Multi-graph
Halve-edge graph
Labeled graph
Weighted graph
Property graph
Labeled property graph
Hypergraph
RDF
RDF*
edge only connects one node

## Slide 8: Graph models
Undirected graph
Simple graph
Multi-graph
Halve-edge graph
Labeled graph
Weighted graph
Property graph
Labeled property graph
Hypergraph
RDF
RDF*
Kitchen
Toilet
labels
directed edges

## Slide 9: Graph models
Undirected graph
Simple graph
Multi-graph
Halve-edge graph
Labeled graph
Weighted graph
Property graph
Labeled property graph
Hypergraph
RDF
RDF*
Kitchen
Toilet
labels
weighted, directed edges
3

## Slide 10: Graph models
Undirected graph
Simple graph
Multi-graph
Halve-edge graph
Labeled graph
Weighted graph
Property graph
Labeled property graph
Hypergraph
RDF
RDF*
directed edges
key-value pairs
Area: 12 m2
Area: 1 m2
Distance: 5m

## Slide 11: Graph models
Undirected graph
Simple graph
Multi-graph
Halve-edge graph
Labeled graph
Weighted graph
Property graph
Labeled property graph
Hypergraph
RDF
RDF*
Kitchen
Toilet
Labels
directed edges
key-value pairs
Area: 12 m2
Area: 1 m2
Distance: 5m
Adjacent zone

## Slide 12: Graph models
Undirected graph
Simple graph
Multi-graph
Halve-edge graph
Labeled graph
Weighted graph
Property graph
Labeled property graph
Hypergraph
RDF
RDF*
ex:
Kitchen
ex:
Toilet
(s,p,o) structure
directed edges
unique resource identifiers
ex:AdjacentZone

## Slide 13: Graph models
Undirected graph
Simple graph
Multi-graph
Halve-edge graph
Labeled graph
Weighted graph
Property graph
Labeled property graph
Hypergraph
RDF
RDF*
Kitchen
Toilet
edges can join multiple nodes
Living room
Garden
Adjacent zone
Storage room
Adjacent zone

## Slide 14: Graph models
Undirected graph
Simple graph
Multi-graph
Halve-edge graph
Labeled graph
Weighted graph
Property graph
Labeled property graph
Hypergraph
RDF
RDF*
Kitchen
Toilet
Labels
directed edges
key-value pairs
Area: 12 m2
IRI: ex:Kitchen
Area: 1 m2
IRI: ex:Toilet
Distance: 5m
IRI: ex:AdjacentZone
Adjacent zone

## Slide 15
We need to compare
RDF with other graph models
with Labeled Property Graphs

## Slide 16: Qualitative
Relationships
Ontologies
Query language
Attributes
Security
Interoperability
Other measures
Quantitative
Graph density
Nodes
Edges
Query execution times
Storage

## Slide 17: Open Smart Home
Consisting
Building information model
Sensor data
RDF Turtle format
- Using BOT, PRODUCT and PROPS ontologies
Schneider, G.F. & Rasmussen, M.D. (2018)
http://doi.org/10.5281/zenodo.1244602

## Slide 18
Data preparation
RDF
LPG (NSMNTX)
Custom LPG
NSMNTX
Manual conversion
Original dataset
N
v
k
N
k: v

## Slide 19
Data preparation
RDF
LPG (NSMNTX)
Custom LPG
NSMNTX
Manual conversion
Original dataset
Kitchen

## Slide 20
What are the differences?

## Slide 21
The fundamental differences between the RDF and LPG models have influence on what and how we can model our data.

## Slide 22: Attributes
LPG can hold attributes on nodes
RDF is more atomic, but also more expressive
Kitchen
Wall
Type: NamedIndividual
Type2: Space
Type3: Kitchen
Label: “Kitchen”@en
Room number: “1”
Area: “15”
Name: “Kitchen of Alex”
Volume: “45”
Type: Element
Name: “Load bearing wall”
Color: “White”
Width: “300”
Length: “3000”
Adjacent element
LPG

## Slide 23: Attributes
LPG can hold attributes on nodes
RDF is more atomic
:Kitchen
:Wall
:Named Individual
:Kitchen
:Space
“Kitchen”@en
“Kitchen of Alex”
“1”
“15”
“45”
“Load bearing wall”
“White”
:Element
“300”
“3000”
:adjacentElement
:name
:roomNumber
:type
:type
:area
:volume
:type
:type
:width
:length
:color
:name
RDF

## Slide 24: Attributes
LPG can hold attributes on edges and therefore qualify the relationship between two nodes.
Since RDF doesn’t have this construct, we need workarounds.
Sensor
Kitchen
Observation
Quantity: Temperature
Time: 2020-06-04T10:00:00
Value: 21
Unit: degree Celsius
LPG

## Slide 25: Attributes
LPG can hold attributes on edges and therefore qualify the relationship between two nodes.
Since RDF doesn’t have this construct, we need workarounds.
- Singleton property
:Sensor
:Kitchen
:Observation1
:Observation1
“2020-06-04T10:00:00”
“21”
:Temperature
:degree
Celsius
:Quantity
:Unit
:Time
:Value
:Observation
:Type
RDF

## Slide 26: Attributes
LPG can hold attributes on edges and therefore qualify the relationship between two nodes.
Since RDF doesn’t have this construct, we need workarounds.
Singleton property
Intermediate node
:Sensor
:Kitchen
:Observation1
“2020-06-04T10:00:00”
“21”
:Temperature
:degree
Celsius
:Quantity
:Unit
:Time
:Value
:Observation
:Type
:Measures
:Location
RDF

## Slide 27: Attributes (weighted edges)
Weighted edges can unlock new possibilities for smart home cases, such as using network analysis algorithms.
“What is the shortest route from the Kitchen to the Living room?”
Kitchen
Dining
Adjacent zone
Distance: “3”
Living
Distance: “2”
Adjacent zone
Hall
Distance: “1”
Adjacent zone
Adjacent zone
Distance: “3”

## Slide 28: Multiple instances of a relationship
LPG can identify multiple instances of a relationship.
In RDF, this is impossible, because this relationship is defined by a URI.
Sensor
Kitchen
Observation
Observation

## Slide 29: Multiple instances of a relationship
LPG can identify multiple instances of a relationship.
In RDF, this is impossible, because this relationship is defined by a URI.
:Sensor
:Kitchen
:Observes
:Location
:Observes
:Location
:Observation
:Observation1
:Observation2
:Type

## Slide 30: Multivalued properties
In RDF, multiple triples could be created with the same subject and predicate, but with a different object.
In LPG, it’s impossible to create multiple properties with the same ‘key’ but with different attributes.
:Kitchen
“Alex”
:Restricted
“Bob”
“Lisa”
:Restricted
:Restricted

## Slide 31: Multivalued properties
In RDF, multiple triples could be created with the same subject and predicate, but with a different object.
In LPG, it’s impossible to create multiple properties with the same ‘key’ but with different attributes.
:Kitchen
Restricted: “Alex”
Restricted: “Bob”
Restricted: “Lisa”
:Kitchen
Restricted: [“Alex”, “Bob”, “Lisa”]

## Slide 32
Different from LPGs, RDF stores typically support ontology modeling languages RDFS and OWL2 DL.

## Slide 33
Health monitoring
IoT data integration
Activity recognition
Social media integration
Energy efficiency
Indoor environmental quality
Home automation
Building performance monitoring
Different domain knowledge
Many stakeholders
Siloed data

## Slide 34: Ontologies
They store domain knowledge
Facilitate interoperability
Enable deeper reasoning
RDF
has a rich ecosystem of creating, using and sharing ontologies
LPG
Using OWL/RDFS constructs in Neo4j is more cumbersome
Shared
Formal
Explicit

## Slide 35
RDF ♥ SPARQL
LPG ♥ Cypher & GQL & GSQL & PGQL &

## Slide 36: Are they really that different?
Constructs
Keen, A.: SPARQL and Cypher Cheat Sheet (2018)

## Slide 37: Are they really that different?
Constructs
Graph creation
Keen, A.: SPARQL and Cypher Cheat Sheet (2018)

## Slide 38: Are they really that different?
Constructs
Graph creation
Object and pattern matching
Keen, A.: SPARQL and Cypher Cheat Sheet (2018)

## Slide 39
Some other measures
Support
Security
Interoperability
Closed vs open world assumption
Index based vs navigational

## Slide 40
What about the quantitative differences?

## Slide 41
Complexity
Kitchen
Measure | RDF | LPG (NSMNTX) | Custom LPG
Nodes | 27 | 16 | 2
Edges | 26 | 15 | 1
Graph Density | 0,037 | 0,063 | 0,5
File size | 7 kb |  | 2 kb
Measure | RDF | LPG (NSMNTX) | Custom LPG
Nodes | 719 | 475 | 115
Edges | 1332 | 507 | 171
Graph Density | 0,0026 | 0,0023 | 0,013
File size | 106 kb |  | 29 kb

## Slide 42
Queries (in Cypher)
Kitchen
Return all nodes
MATCH (n) RETURN n
Return all nodes and edges
2. MATCH (n)-[r]->(m) RETURN n,r,m
Return all nodes and edges of type ns0__AdjacentElement
3. MATCH (n)-[r:ns0__AdjacentElement]->(m) RETURN n,r,m
Return a list of walls with their length, width and name
4a.MATCH (n)-[:ns3__dimensionsLength]->()-[]->(l),
(n)-[:ns3__dimensionsWidth]->()-[]->(w),
(n)-[:ns3__identityDataName]->()-[]->(s)
RETURN n.uri, l.sch__value, w.sch__value, s.sch__value
4b.MATCH (n)-[]->(m)
RETURN m.uri, m.ns2__name,m.ns2__width,m.ns2__length

## Slide 43
Query Execution Time
Kitchen
Query | LPG (NSMNTX) Before caching | LPG (NSMNTX) After caching | Custom LPG Before caching | Custom LPG After caching
1 | 23.8 ms | 2.6 ms | 13.8 ms | 1.3 ms
2 | 32.5 ms | 4.4 ms | 16.8 ms | 1.6 ms
3 | 27.8 ms | 1.8 ms | 18.0 ms | 1.6 ms
4 | 23.7 ms | 1.7 ms | 11.5 ms | 1.2 ms

## Slide 44
Summary
Attributes on nodes
LPGs can attach attributes to nodes. RDF can store similar (or more expressive) information by creating new triples.
Attributes on edges
LPGs can attach attributes to edges. RDF needs complex workarounds to store the same information.
Relationships
RDF can have multivalued properties. LPG can have multiple instances of the same relationship.
Ontologies
RDF typically supports RDFS and OWL2. Using these languages in LPGs is more cumbersome.
Query language
RDF has a standardized query language. LPGs have different query languages based on the vendor.

## Slide 45
Summary (2)
Complexity
LPGs are usually less atomic than RDF graphs, and therefore visually less complex.
Query execution time
In the queries we tested, the custom LPG outperformed the RDF import in query execution time.
File size
Due to the lower complexity, the file size of the LPGs is significantly lower.

## Slide 46
LPG
Fast
Good for large datasets, time-series data, path analysis, deep graph traversals
Good for single-stakeholder environments
RDF
International standard
Good for interoperability amongst multiple stakeholders
Good for domain knowledge sharing

## Slide 47
Thank you.
Alex Donkers MSc – PhD Candidate at Eindhoven University of Technology – a.j.a.donkers@tue.nl