## Slide 1
Maryam Daneshfar, Timo Hartmann, Jochen Rabe
Technische Universität Berlin
A GIS-based Ontology for Representing the Surrounding Environment of Buildings to Support Building Renovation
LDAC 2020, Online
17th June 2020

## Slide 2
Building renovation is an inter-disciplinary task
Building renovation projects usually focus on data collection and analysis in individual building level
Surrounding and environment of the building affect its renovation process
The context where the building is located in is important
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Architecture, Construction (BIM)
Geospatial domain
(GIS)
Notes: BIM GIS integration
Effect of surrounding data in renovation process

## Slide 3
The objective is:
to conceptually define what kind of geospatial data are required for the renovation process
to represent the possibility of using data from geospatial domain in the renovation process
to get more attention toward geospatial domain in AEC and specifically in building renovation projects
To help in decision making to control cost and quality
Ontology is an approach for “an explicit specification of a conceptualization”
Gruber T-R (1995)
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work

## Slide 4
Geospatial domain tries to model real-world in a simplified manner
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Physical model
Computational model
Cognitive model
Logical model
Representational model
Real-world
Human’s perception
Expressing human’s perception in an explicit formal structure
Object view/Field view
Algorithms/Raster, Vector
Low level
High level
General concpets
Specific concpets
Domain
Task
Urban ontology
Building renovation
Notes: Example for objects, processes, relations, events

## Slide 5
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Fonseca F et al. (2000)
Urban ontology
Objects
Relations
Processes
Events
Bona fide boundaries
Fiat boundaries
Notes: Example for objects, processes, relations, events

## Slide 6
France-Mensah et al. (2019) methodology
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Ontology specification
Knowledge acquisition
Conceptualization and implementation
Validation
Purpose
Scope
Intended end-users
Intended use
Defining use cases
Literature review
Brainstorming
Interviewing experts

## Slide 7
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Use case | Surrounding environment data | Source
Site planning | Building block, road, railway, vegetated area, single tres, parking lot, monument, societal data … | Göcer et al. 2016
Building energy modeling (BEM) | Weather data (*.epw weather file for energy modeling in EnergyPlus) | Crawley 1998 Huang 2011
Acoustic comfort analysis | Road, walkway, railway, railway station, airport location, playground and park, running water, pool, lake, noise map | Herranz-Pascual et al. 2017 Kang et al. 2016
Air quality comfort analysis | Road, building , CO2 emission map | Leung 2015, Li et al. 2009
Thermal comfort analysis | Weather data, building, single tree, energy consumption behavior of the occupants, renewable energy sources | Aghniaey et al. 2018 Humphreys et al. 2000
Lighting comfort analysis | Building, tree | Jung 2018 [24]
Notes:   This is an initial list of the use
  Description of site planning
  Description of BEM

## Slide 8
Examples of use cases
Site planning
Considerations for selection of method for 3D laser scanning or thermal scanning of the building
High dense built area
Single trees
Building energy modelling
Weather data
Urban climate
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work

## Slide 9
France-Mensah et al. (2019) methodology
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Ontology specification
Knowledge acquisition
Conceptualization and implementation
Validation
https://depositonce.tu-berlin.de/handle/11303/11235
The OWL of the ontology is available online:
Population-related
Process
Energy-related
Environment-related
Object
Energy network
Vegetation
Built area
Traffic network
Water

## Slide 10
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Object
Vegetation
Park
Single tree
string
double
double
string
Built area
Parking space
Parking lot
Parking
Monument
Parcel
District
Building block
Building
Landuse type
double
Construction regulation
double
double
double
double
string
string
string
int
parkName
parkArea
treeHeight
treeCrownSize
treeSpecies
hasParcel
districtName
districtArea
landUseTye
hasLanduseType
containsMonument
hasConstraint
containsPrking
parlingArea
containsBUildingBlcok
hasBuilding
buildingBlockArea
buildingHeight
buildingArea
facadeMaterial
numberOfFloor
double
Notes: Description of some data and their attributes

## Slide 11
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Traffic network
Railway
Airport
Railway station
Walkway
Road
string
RailwayType
double
string
string
RoadType
string
double
Object
Water
River
Lake
Pond
string
double
double
double
string
string
hasRoadType
hasRailwayType
roadType
railwayType
railwayWidth
airportName
railwayStationName
double
walkwayWidth
roadWidth
riverWidth
riverName
pondArea
pondName
lakeName
lakeArea
Energy network
EnergyType
string
hasEnergyType
energyType

## Slide 12
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Population-related
Process
Energy-related
Environment-related
Wind power potential
Renewable energy potential
Energy consumption
Geothermal potential
Solar energy potential
Photovoltaics
Solar thermal
Biomass potential
Energy type
hasEnergyType
string
energyType
Energy consumption value
hasEnergyConsumptionVal
double
energyConVal
Wind power electriciy feed
hasWindPowerElectricityFeed
double
windPowerElectricityFeedVal
Depth
hasDepth
double
depth
Withdrawl performace value
hasWithdrawlPerformance
double
windPowerElectricityFeedVal
Electricity generation potential
hasElectricityGenerationPotential
double
electricityGenVal
Solar potential heat electricity feed
hasSolarPotentialHeatElectricityFeed
double
solarPotentialHeatElectricityFeedVal
Solar potential electricity feed
hasSolarPotential ElectricityFeed
double
solarPotentialElectricityFeedVal
Notes: Description of some processes and their attributes

## Slide 13
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Process
Environment-related
Population age
Population age range
hasPopulationAgeRange
co2Val
double
Energy-related
Population-related
Population density
Population education level
Population age range value
hasPopulationAgeRangeVal
populationAgeRangeVal
Population density value
hasPopulationDensityVal
double
populationDensityVal
Education level
hasEducationLevel
educationLevelVal
string
Noise level
CO2 emission
Weather
CO2 value
hasCo2EmissionVal
double
Noise level value
hasNoiseLevelVal
noiseLevelVal
double
Weather file
isLinkedTo
Weather data
fileContains
File format The file format which is accepted by the energy modeller e.g *.epw file format
hasFormatConstraint
double
int
double
double
windDirection
humidity
windSpeed
temperature
Object
District
Building block
Building
hasProcess
hasBuilkding

## Slide 14
Implications for practice:
  this ontology can be used as a tool for decision makers in the renovation process. It helps energy experts, architect and planners to understand the urban context and get more accurate results and less cost
Implications for research:
  this can be used as a basis for data integration of BIM and GIS for renovation purposes
  Investigating how developing this ontology and integrating it with other ontologies can contribute to the linked data
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work

## Slide 15
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Objective was to conceptually define what kind of geospatial data are required for the renovation workflow
  This part has been done based on use case definition, brainstorming, literature review and incorporating experts
  Future task: involving other experts, defining new use cases
Objective was to support planners, decision-makers, and experts involved in the renovation process
  To validate and check the competency of the ontology
  Presenting a proof of concept
Work in Progress

## Slide 16
Introduction
Objectives
Theoretical framework
Method
Result
Discussion/Future work
Building Topology Ontology
(BOT)
CityObject
CityGML
Ontology for Managing Geometry (OMG)
Future Work
      Existing ontologies

## Slide 17
Thanks for you attention
This research project is funded under the European Union’s program H2020-NMBP- EEB-2018, under Grant Agreement no 820553.

## Slide 18
Key references
Gruber T-R (1995) Toward principles for the design of ontologies used for knowledge sharing? International Journal of Human-Computer Studies, 43(5-6), 907–928.
Fonseca F, Egenhofer M, Davis C, Borges K A (2000) Ontologies and knowledge sharing in urban GIS. Computers, Environment and Urban Systems, 24(3), 251–272.
France-Mensah, J., & O’Brien, W. J. (2019). A shared ontology for integrated highway planning. Advanced Engineering Informatics, 41, 100929.